In order to pass the whole set of 19 args to the script one must group in two main categories: 1) 'fixed' values, i.e., not changing from one pass to another, for a given engine, and 2) values that change with each pass according to actual engine-powertrain conditions.
In order to make the things easier, i.e., to decrease the call effort the first category is to be stored within a list, built once and passed with every call.
The 'fixed' values are as following (passed within a list exactly in this order):
1. the transmission final ratio 'xi_f',
2. the slipping factor 's_f',
3. the wheel rolling radius 'r_d',
4. the engine maximum speed 'n_max',
5. the engine maximum output, ‘P_max’,
6. the engine type, ‘type’,
7. the transmission overall efficiency, ‘eta_t’,
8. the engine maximum efficiency, ‘eta_max’,
9. the vehicle mass, ‘m_a’,
10. the rolling drag coefficient, ‘c_r’,
11. the wind drag coefficient, ‘C_d’,
12. the vehicle frontal area, ‘A_f’,
13. the air density, ‘ro_a’,
14. the fuel burning value, ‘Q_f’ (in Joule/liter),
15. the fuel density, ‘ro_f’.
  The second category (‘volatile’ values, in this order) is:
16. the vehicle initial speed, ‘v_init’,
17. the gearbox ratio, ‘xi_g’,
18. the acceleration, ‘a’,
19. the time, ‘t’.
At RL agent level the specific fuel consumption script is to be invoked in an API-style, presented in the ‘sfc_call.py’ file.
If, by passed args, vehicle speed leads to an engine speed greater than maximum possible the program displays a warning and exists. Same is true for power/output.
I recommend to read every function and method docstring carefully. Also every comment is meant for further clarification.